## Slide 1: Accurate Activation on Wrist Raise for Smartwatches
Sheng Shen ECE@UIUC

## Slide 2: Smartwatch: More than a watch
Time

## Slide 3: Smartwatch: More than a watch
Time
Sensors Accelerometer, Gyroscope
Compass
Heartrate

## Slide 4: Smartwatch: More than a watch
Time
Sensors Accelerometer, Gyroscope
Compass
Heartrate
Wireless Technology Bluetooth, Wi-Fi, GPS

## Slide 5: Smartwatch: More than a watch
Functionality + Interaction

## Slide 6: Battery: Always a pain!

## Slide 7: Battery: Always a pain!
Biggest Battery Drainer: Screen

## Slide 8: Solutions
Keep screen dim all the time
Require a ‘tapping’ to start operating 

## Slide 9: Solutions
Keep screen dim all the time
Require a ‘tapping’ to start operating 
Opportunistically turn screen on
Detect wrist raise motion and activate 

## Slide 10: Problem with current Activation on wrist raise
False positives
Delay
Not adaptive
Black box

## Slide 11: Problem with current Activation on wrist raise
False positives
Delay
Not adaptive
Black box
Build our own technique!

## Slide 12: Things to keep in mind…
Need to run in the background continuously! Use energy-saving sensors – accelerometer, gyroscope, etc.

## Slide 13: Things to keep in mind…
Need to run in the background continuously! Use energy-saving sensors – accelerometer, gyroscope, etc.
Users will not tolerate any delay! Detection must be real-time

## Slide 14: Things to keep in mind…
Need to run in the background continuously! Use energy-saving sensors – accelerometer, gyroscope, etc.
Users will not tolerate any delay! Detection must be real-time
Need to run on watch… Algorithms must be lightweight and fast

## Slide 15: Demo

## Slide 16: Area of interest When we raise wrist…
The watch faces human eyes.

## Slide 17: Area of interest When we raise wrist…
The watch faces human eyes. How to detect if watch is in AOI?

## Slide 18: Motion sensors: a deeper look
X
Y
Z is pointing out of watch face
Z
Accelerometer Measures acceleration along X, Y and Z (includes gravity)
Gyroscope Measures rotational speed around X, Y and Z

## Slide 19: Area of interest Gravity should tell us that!
X
Y
Z is pointing out of watch face
Z
Gravity
Assume the watch is stationary…
Some gravity along –Z
Some gravity along –Y
Others along +/- X, but should not too much

## Slide 20: AOI detection using accelerometer
Arm on body left side
Wrist raised

## Slide 21: AOI detection using accelerometer
Arm on body left side
Wrist raised
For any time window with length W
Min(Accel Y) > th1
Min(Accel Z) > 0
Min(Accel X) > th2
Max(Accel X) < th3

## Slide 22: AOI information is not sufficient…
Reach for a book on the shelf vs. Raise wrist to see time while walking

## Slide 23: AOI information is not sufficient…
Reach for a book on the shelf vs. Raise wrist to see time while walking
Acceleration tells us both these two are in AOI, but only the second one is correct

## Slide 24: AOI information is not sufficient…
Reach for a book on the shelf vs. Raise wrist to see time while walking
Acceleration tells us both these two are in AOI, but only the second one is correct
Opportunity: watch orientation tends to be stable for a while when we look at it

## Slide 25: AOI stability detection using gyroscope
Left: Reach books
Right: Look at time while walking

## Slide 26: AOI stability detection using gyroscope
Left: Reach books
Right: Look at time while walking
Abs(Gyro X, Y, Z) < th4

## Slide 27: Further details
How to choose parameters? - Collected data from 3 different users - Derived thresholds that has highest classification rate in distinguishing intentional wrist raise from other motions
How to adapt to different users? - We have implicit ground truth data for wrist raise for each user - Adapt the thresholds over time

## Slide 28: Future work
Test on more users and report accuracy
Need user feedback to evaluate latency
Report energy usage (e.g. with different sampling rates)

## Slide 29: Thanks!
sshen19@Illinois.edu